## Slide 1: CLIC structure collaboration meeting
G. Riddone, AB-RF
2008.07.04

## Slide 2: Agenda
Status of the production and test program (CERN, KEK, SLAC)
Testing of PETS (CERN, SLAC)
Design of quadrants and disks (KEK)
Pulse compressor for Nextef at KEK

## Slide 3: Status – x-band ac. structures

## Slide 4: CLIC vg1 quadrant damped TD18_vg2.4_quad#3
For the preparation decision to follow the same procedure as SLAC for the disk version
Done at CERN: dimensional control, Rf check, cleaning, assembly test  shipping to SLAC on 24.06
To be done at SLAC: heat treatment, brazing of the cooling pipes, SEM, baking, final assembly, rf checks
CERN agreement on additional SLAC costs
Question: Tuning (yes/no)  decision postponed after heat treatment
  Heat treatment at CERN done for #1 (same cycle as for SLAC)  then rf check, dimensional control, tuning test

## Slide 5: C10 damped structures
Cern agreement

## Slide 6: CLIC vg1 structures

## Slide 7: Status - PETS
Received bars for 12 GHz test  Dimensional control: OK (+/- 10 mm)

## Slide 8: PETS 11.4 GHz w/o damping mat.
Done at CERN before shipping to SLAC
  Dimensional control of two bars
  Brazing and preparation of the couplers
  Assembly test
  Rf check
  Cleaning of all pieces
  EB welding of the bars
  Tank and couplers assembly
  Final EB welding: 07.07
  rf test + UHV test
PETS shall be shipped to SLAC in CW28 at the latest

## Slide 9: 11.4 GHz Loads (x4) for KEK
11.4 GHz Loads (x4) for KEK 2 with KEK flanges and 2 with SLAC flanges
  Rf design done
  Mechanical design done
  Call for tender under way
  Fabrication: by end of October
  Supply of the material: shipped to CERN, not received yet
SLAC flanges: pieces available at CERN, brazing and assembly by end of July