## Slide 1
Comparison of High Gradient Performance in Varying Cavity Geometries
T. Higo#, T. Abe, Y. Arakida, S. Matsumoto, T. Shidara, T. Takatomi, M. Yamanaka, KEK, Ibaraki, Japan Y. Higashi, OKINAWA Institute of Science and Technology Graduate University, Okinawa, Japan A. Grudiev, G. Riddone, W. Wuensch, CERN, Geneva, Switzerland
BDR evolution as time
Fast Processing Slow
Undamped Damping Damped
T24 >> TD24 >> TD24R05
Structure | TD18 | TD24 | TD24R05
Eacc [MV/m] | 79 ~ 120 | 94 ~ 102 | 94 ~ 102
DT [C] | 29 ~ 47 | 25 ~ 21 | 21 ~ 19
Cell prod.
DB & Brazing
VAC bake at 650C
RF check in cleanroom
Oversea shipping
Install to Nextef
Production and installation for setup at Nextef
TD24R05
TD24
T24
Design with reduced magnetic field
Abstract
Five types of CLIC prototype TW accelerator structures were high-gradient tested up to 100 MV/m level since 2008 at KEK.
It was found that the ramping speed is slow in the structures with opening ports for HOM damping with magnetic coupling became slow. This indicates the role of the magnetic field on vacuum breakdowns.
The breakdown rate, BDR, of the un-damped structure T24 was very low, clearly meeting the CLIC requirement of a few 10-7/pulse/m at 100 MV/m. However, the BDR of the damped structures showed much higher than undamped ones.
One of the structures showed hot spots, where frequent breakdowns appear in particular regions of the structure. It indicates a mechanism reflecting not only the geometry or material characteristics but also the local features acquired after completion or even during the running.
BDR vs pulse width
BD timing
Breakdown and pulse width
BDR scales Tp6 while BD timing in the pulse is flat.
 Breakdown trigger is not developed within a pulse but due to the accumulated effect over many pulses.
TD24R05
Probably less processing but also some mechanism related to the hot spot made poor performance, especially even later time.
Hot spot
Distribution of BD position
Before (Hot spot appeared) After
Frequent breakdown spots at both ends!
In the damped structures the gradient level such as 80 MV/m seems feasible if based on the present technology. One of the key parameters is the surface magnetic field, Hs. If high BDR is inevitable due to the high Hs, we need to introduce such structure as choke-mode type where no big enhancement of Hs is needed. The study is on-going in collaboration including Tsinghua University.
Another new issue is the hot spot. The mechanism and the technology to suppress such cases should be studies. We have been preparing studies with simple geometries in a small-sized setup at Nextef at KEK.
Concluding remarks
Processing as time
Processing
as number of BD’s
Need more breakdowns in damped structures and associated process time.