## Slide 1: Electron / Positron Injector Linac
Kazuro Furukawa
<kazuro.furukawa@kek.jp>
for Injector Linac

## Slide 2: Mission of electron/positron Injector in SuperKEKB
40-times higher Luminosity
  Twice larger storage beam  Higher beam current at Linac
  20-times higher collision rate with nano-beam scheme
     Low-emittance even at first turn  Low-emittance beam from Linac
     Shorter storage lifetime ( Higher Linac beam current)
Linac challenges
  Low emittance e-
    with high-charge RF-gun
  Low emittance e+
    with damping ring
  Higher e+ beam current
    with new capture section
  Emittance preservation
    with precise beam control
  4+1 ring simultaneous injection
Linac Overview
Notes: Higher Injection Beam Current
  To Meet the larger stored beam current and shorter beam lifetime in the ring
  4~8-times larger bunch current for electron and positron
  Reconstruction of positron generator, etc
Lower-emittance Injection Beam
  To meet nano-beam scheme in the ring
  Positron with a damping ring
  Electron with a photo-cathode RF gun
  Emittance preservation by alignment and beam instrumentation
Quasi-simultaneous injections into 4 storage rings
  SuperKEKB e–/e+ rings, and light sources of PF and PF-AR
  Improvements to beam instrumentation, low-level RF, controls, timing, etc

## Slide 3: Linac Upgrade for SuperKEKB
Higher Injection Beam Current
  To Meet the larger stored beam current and shorter beam lifetime in the ring
  4~8-times larger bunch current for electron and positron
Lower-emittance Injection Beam
  To meet nano-beam scheme in the ring
  Positron with a damping ring, Electron with a photo-cathode RF gun
  Emittance preservation by alignment and beam instrumentation
Quasi-simultaneous injections into 4 storage rings (PPM)
  SuperKEKB e–/e+ rings, and light sources of PF and PF-AR
  Improvements to beam instrumentation, low-level RF, controls, timing, etc
4.0 GeV e+ 4nC x 2
3.5 GeV
10nC x 2 (prim. e-)
5nC x 2 (inj. e-)
1.1 GeV
Damping Ring
circ. 136 m
ECS
high current
gun
Energy-spread
Compression System
Bunch
Compressor
7.0 GeV e-
5nC x 2
low emittance
RF gun
SuperKEKB injector Linac
e+ target &
L-band+LAS
capture section
50 Hz (e+ or e-)
pulse-by-pulse
mode switching
S-band
linac
2.5 GeV e-
0.1nC x 1
PF
HER
LER
PF-AR
6.5 GeV e-
C-band
modules
3T
RF gun
Ir5Ce
FC

## Slide 4: Linac Schedule Overview (to be updated)
RF-Gun e- beam
commissioning
at A,B-sector
Qe- = 5nC
e- commiss.
at A,B,J,C,1
Qe- = 5nC
e+ commiss.
at 1,2 Qe+ = 0.5nC (FC, DCS, Qe- 50%)
e- commiss.
at 1,2,3,4,5 Qe- = 5nC
non damped e+ commiss.
at 1,2, 3,4,5 Qe+ = 4nC
e- commiss. pulse-switch
at A→5 Qe- = 5nC
damped e+ commiss.
at 1→5 Qe+ = 4nC
e- commiss.
at A→5 Qe- = 5nC
PF-AR e-
commiss.
: Electron
: Positron
: Low current electron
1 nC
2 nC
4 nC

## Slide 5: Fire during flux concentrator development
One of small problems – Cables burned by 20cm

## Slide 6: SLAC-SuperKEKB Workshop (Injector Linac)
Injector commissioning and issues 30'
  Speaker: Masanori Satoh (KEK)
Photo-cathode RF gun 20'
  Speaker: Takuya Natsui (KEK)
Positron source 30'
  Speaker: Takuya Kamitani (KEK)
Timing synchronization 20'
  Speaker: Hiroshi Kaji (KEK)
Linac alignment 20'
  Speaker: Toshiyasu Higo (KEK)
Beam optics design for simultaneous injection 20'
  Speaker: Takako Miura (KEK)

## Slide 7: Questions and Answers
PEDD dependent on beam repetition?
  SLAC study was on single-pulse energy density
    may need further investigation
Fiber loss monitor blackening around target?
  Can be replaced routinely
Diamond loss detector?
  Is worth comparing in the future
Orbit stability tolerance against beam size?
  Pinhole 2mm and beam sigma 0.3mm are possible Beam orbit jitter will be studied, as well as for emittance preservation
Rotating target/spoiler?
  Should be studied for the beam current larger
Frequency synchronization btw. linac/ring?
  All SKEKB frequencies are generated from common freq. with ring circumference compensation
Beam charge variation pulse-pulse?
  Can be important
  Technically possible with different event assignment
  Means different injection modes with different orbit stabilization for wakefield
Target quad – pulsed ?
Beam jitter should be small
DR extraction angle jitter
  Offset injection position/angle jitter should be small

## Slide 8: Several Workshop around Injector Linac
Technology choice for beam position monitor (BPM)
  Indispensable for emittance preservation
  ~10micron precision (~100micron in KEKB linac), about 100 BPMs, event controls
  Experts from SLAC, Steve Smith and Andrew Young
  Many valuable discussions for filter design, digital signal processing, etc.
  One of the developments was chosen for performance, operation, and budget
Laser and photo-cathode RF gun workshop
  6 presentations, 16 participants
  The same objectives of low emittance and higher stability
  Injector linac is unique on higher beam charge and lower energy spread
  Should exchange technology/information continuously
Accelerator structure processing workshop
  22 participants
  Many discussions on duration (more than a month), and the system
  No baking necessary, longer processing and better monitors, better interlock needed

## Slide 9: Improved beam optics design
Pulsed quad addition – Simultaneous injection
FODO → Doublet – Emittance preservation
Orbit correction simulation
Further emittance preservation even with alignment tolerances
Optimization for budget …

## Slide 10
low emittance
RF gun
A
B
C
1
2
3
4
5
1.5 GeV e-
e+ target
KEK e-/e+ Injector LINAC
e-:Chicane
10 nC x 2 (for LER)
5 nC x 2 (for HER)
0.3 nC x 1 (for AR)
0.3 nC x 1 (for PF)
1.1 GeV
DR
Decelerate
e+ target
5
4
3
2
1
C
e-
e+
1.1 GeV
4.219 GeV
1.5 GeV
same energy
e-/e+ beams are delivered to 4-rings with different current & energy.
Beam acceleration modes must be switched by 50 Hz pulse-by-pulse for top-up injection.
Beam optics should satisfy the fast beam-mode switching.
HER: 7 GeV e-
AR: 6.5 GeV e-
PF: 2.5 GeV e-
LER: 2.5 GeV e+
5 nC x2
0.3 nC x1
0.3 nC x1
4 nC x2

## Slide 11: Result of e-p fitting
e+
e-

## Slide 12: Emittance Preservation
If Device is off center of the beam
  Focusing magnet (quad) kicks the beam bunch
  Accelerating structure (cavity) excites wakefield, to bend the tail
Distorted bunch in banana shape
  Emittance dilution or blow-up
  Depending on the beam optics and the beam charge
Orbit correction is crucial to preserve the emittance
Focusing Magnet
Beam
Accelerating Structure
Transverse distribution in time direction
Sugimoto et al.

## Slide 13: Emittance Dilution
Offset injection may solve the issue
Orbit have to be maintained precisely
100 samples
Mis-alignment leads to Emittance blow-up
Sugimoto et al.
Orbit manipulation compensates it

## Slide 14
Alignment Error vs. Emittance Growth
Calculated by H. Sugimoto
Zoom
Positron is transported from DR outlet to LINAC end.
Alignment error is given in quads and cavities.
The orbit correction is performed by assuming the center of the quads and BPM are exactly the same.
Initial Emittance@Outlet of DR =6.5 mm / 89 mm (Vertical / Horizontal)
Vertical
Horizontal
e+ norm.  at LINAC-end should be less than
20 m / 100m ( Ver. / Hor.)
Triplet and doublet give almost same results.
In triplet and doublet, misalignment of 300m is acceptable.
In FODO lattice, significant emittance growth is seen.
<Tracking Condition>

## Slide 15: Positron Source
High current positron is required
Positron capturing with flux concentrator (FC) and large aperture s-band structure (LAS)
Deceleration field to reduce satellite bunches
Pinhole beside target for electron beam
Protection system with beam spoilers

## Slide 16: Positron beamline under construction
KLY
1-5
KLY
1-6
SLED
SLED
LAS 14 MV/m
deceleration & phase slip & acceleration
LAS 10 MV/m
acceleration
Solenoids
target
+FC
primary e- 3.2 GeV, 10 nC x 2 bunch, 50 Hz
tungsten target
AMD system (5.0 T x 200mm + 0.4 T x 15m) Flux Concentrator DC solenoids
KLY1 2m LAS x 2 (14 MV/m), aperture 2a = 32 -> 30 mm (typical S-band ~20 mm)
KLY2 2m LAS x 4 (10 MV/m), aperture 2a = 32 -> 30 mm
e+ beam energy at capture section exit : 110 MeV
e+ yield: N(e+)/N(e-) = 49 % at 1.1 GeV DR
Deceleration capture
LAS : Large Aperture S-band structure

## Slide 17: Flux Concentrator Assembly
positron
production
Target
Flux
Concentrator
Bridge
Coils
primary
e- beam
e+ beam
quick detachable power & water connection
to minimize worker's radiation dose
FC assembly

## Slide 18: e+/e- beam switching at target
Flux
Concentrator
e+
5 nC injection e-
10 nC
primary e-
bridge coils
target
beam
hole
pulse ST
DC QM
pulse QM
side view
rear view
e+ on-axis, e- offset -> e- emittance growth by solenoid kick induced orbit
e- on-axis, e+ offset -> e+ yield degradation (50% -> 10%)
target
offset
3.5 mm
2.0 mm
FC offset
7.0 mm
FC aperture
spoiler
target
diameter
4.0 mm
hole
diameter
2.0 mm
solenoid
LAS Accel.
structure
we take this scheme.
Two possible schemes of beam switching by orbit bump
T.Kamitani

## Slide 19: Photo-cathode RF-gun Development
A1 RF-gun (GR_A1) under test
  Big progresses are quasi-traveling wave side-coupled cavity, Ir5Ce photo-cathode, Yb fiber laser
  Longitudinal laser pulse manipulation is necessary for energy-spread and stability management
  Should understand those many new components for real stable operation
  5-nC per bunch was re-confirmed with new configuration
  600-m transport was confirmed (with small charge)

## Slide 21: GR_A1 : 5.1 nC / bunch
Vertical position /mm
Charge /nC
Charge Trend / Stability

## Slide 22: Beam Trend / Stability

## Slide 23: Horizontal / Vertical stability

## Slide 24
600m beam transport from RF-gun with QTWSC

## Slide 25: Virtual Accelerator-based Controls
Multiple closed loops were installed on each PPM VA independently
  Tested at KEKB
ARC
e+ Target
e– BT (PF: 2.5GeV, 0.1nC)
e− Gun
ARC
e+ Target
e+ BT (KEKB: 3.5GeV, 0.6nC)
e− Gun
ARC
e+ Target
e– BT (KEKB: 8GeV, 1.2nC)
e− Gun
Event-based Control System
PF Injection
KEKB-LER Injection
KEKB-HER Injection
Primary e– (4GeV, 10nC)
Dual-layer Controls

## Slide 26
ARC
e– (2.5GeV, 0.2nC)
e− Gun
ARC
e+ Target
e+ (4GeV, 4nC)
e− Gun
PF Injection
SuperKEKB-LER Injection
e– (3.5GeV, 10nC)
ARC
e– (7GeV, 5nC)
e− Gun
SuperKEKB-HER Injection
ARC
e– (6.5GeV, 5nC)
e− Gun
PF-AR Injection
Damping ring
Event-based Control System
Every 20 ms
F.B
F.B
F.B
F.B
F.B
F.B
F.B
F.B
Four PPM VAs at least for SuperKEKB project (maybe with additional PPM VA for stealth beam)

## Slide 27: Summary
Steady progress towards first MR injection in 2015
Will make staged improvements before 2017
Will finish disaster recovery in 2014
Will balance between final beam quality and stable and staged operation
Will select optimized route depending on available resources

## Slide 28
SuperKEKB
dual rings
Mt. Tsukuba
Injector Linac
PF-AR
PF
Thank you

## Slide 30
Real Accelerator
EPICS Controls
Independent PPM Parameters
Common Parameters
Event Synchronous Controls
Simulation Virtual Accelerators
Display and Analysis
PPM Virtual Accelerators
System Construction
Multiple
Multiple
Multiple

## Slide 31: e- beam
20 mmmrad, 0.08% energy spread, 5 nC, two bunch
Component Alignment
& BBA
e- RF gun
(5 nC)
Offset injection
@ Sector C-5
Bunch compression @ J-ARC
BNS damping
@ Sector A-B
Uniform longitudinal beam distribution
High precision monitor

## Slide 32
20 mmmrad, 0.07% energy spread, 4 nC, two bunch
Component Alignment
& BBA
e- RF gun
(10 nC)
Flux concentrator
Large aperture
S-band structure
Damping ring operation
Timing system
/Bucket selection
e+ beam

## Slide 33: ビームライン詳細
陽電子ター ゲットから LTR まで
地下と地上 の摺合わせ
各機器の最 終調整と発 注
e+ capture section
matching
section

## Slide 34: まとめ
2 年後の MR 入射コミッショニングに向け、ひとつの Milestone は越えた
震災の影響の懸念をある程度払拭した
SuperKEKB のビーム仕様を満たすための試験の準備が整ってきた
まずは T=0 の 1nC ビームのエミッタンスとエネルギー幅を満足し、さらに大電流ビームのビーム特性達成を目指す
  そのために、機器の安定度向上、ビーム・マイクロ波・タイミング測定、大電流加速、ビーム安定化機構、特にエミッタンス・エネルギー幅制御の確立、などをひとつずつ段階を踏んで進めて行く

## Slide 35: BPM 読み出しの技術選択
Beam position monitor (BPM)
  Emittance preservation に重要となる
  ~10μm の要求分解能 (現在の装置は 50~100μm)
Libera と SLAC の技術を基礎とした新規開発
  それぞれ開発・評価中
SLAC の Steve Smith 氏と Andrew Young 氏に Review 依頼
    SLAC – SuperKEKB の協力の枠組み
  Filter 設計、Dual-bunch 信号処理、System 設計に関して詳細な Comment をもらう (may.22-27, jun.15-18.2013.)
  Reviewer は新規開発を選択
詳細設計の改善中
  予算の関係で当初からの全数設置は避けるが、現在のところ、新規開発が性能、価格、運用、保守の全般で有利として、開発中

## Slide 36: Laser RF 電子銃 Workshop
ATF, cERL, Linac から計 16 人参加、6+ 件の発表
機構内でも共通技術の交換の可能性がある
低 Emittance はほぼ共通目標であるが、Linac で重要な大電流 + 低エネルギー幅は Unique で、そのための技術交換はあまりなかった
安定度などについて、今後とも情報交換の予定
Web を準備する予定

## Slide 37: RF Gun GR_A1 Overall Structure
Oscillator
Regenerative Amplifier
Multipass Amplifier

## Slide 38: Regenerative Amplifier

## Slide 39: Multipass Amplifier

## Slide 40: Quadruple Frequency