## Slide 1: Injector linac status
  Kazuro Furukawa
  for Injector Linac Groups
  <http://www-linac.kek.jp/linac-paper/general/>
  < kazuro.furukawa @ kek.jp >
BPAC November 2020

## Slide 2: Improvements during summer shutdown
Installation of diffractive optical element (DOE, laser profile shaping), laser position stabilization feedback, cathode, etc. for true 50 Hz, cleaning and stabilization
Improvement to master oscillator with more detectors and phase shifters
Upgrade the merger beamline of two guns with 2 pulsed bends, 3 quads, 2 bpms and a chamber for true 50 Hz
Installation of 4 steering magnets and 4 bpms inside of positron capturing section
Replacement of flux-concentrator and nominal operational field (12 kA)
And many other improvements

## Slide 3: Positron yield
Y. Enomoto
After summer
Before summer
Flux concentrator replacement

## Slide 4: Improvements during summer shutdown
Replacement of thermionic gun cathode
Replacement of RF gun cathode (Ir7Ce2), removing heating system
Installation of diffractive optical element (DOE, laser profile shaping), Laser position stabilization feedback
Upgrade of event timing controls for continuous laser cleaning
Preparation for secondary RF gun
Replacement of high power klystron (KL_B4)
Replacement of klystron solenoid power supply (2)
Replacement of thyratron (KL_A1_B, A2, 15, 16, 17, DS, DN)
Installation of noise elimination measure (all 60 units)
Replacement of inverter power supply (KL_17, DS)
Improvement to master oscillator with more detectors and phase shifters
Replacement of driver klystron with solid-state amplifier (SB_B)
Installation of independent amplifier (KL_C8)
Pulse-to-pulse amplitude controls at SHB
Replacement of flux-concentrator and nominal operational field (12 kA)
Installation of 4 pulsed steering magnets and 4 bpms inside of positron capturing section
Replacement of charging circuit for all pulsed magnet power supplies
Replacement of old cables for high power magnet power supplies
Upgrade merger beamline after two guns with 2 pulsed bends, 3 quads, 2 bpms and a new chamber

## Slide 5: Injector linac operation
Injector linac could not allocate machine study time this season up to last week, that was devoted to bt beam study and radiation safety.
Injector linac had limited chance to tune injector beams as we shared startup time for light sources, who cancelled most of beam time before summer.
This week, several study items are being performed.
HER
LER
PF ring
PF-AR

## Slide 6: Investigations and improvements in this week
Discrete vertical orbit
    Discrete orbits observed with light-source injections, that didn’t affect the injection much (?)
  Caused by the combination of magnetic aftereffect and hysteresis of the new pulsed bending magnet to merge two guns, and by the beam pattern (found on Nov.18)
  Would tune the beam pattern in this season
    Further tuning measures during winter shutdown
7-minute orbit variation
    Orbit and charge variation even with laser stabilization, that annoyed the injection tuning.
  Caused by one of the chillers for a optical table (found on Nov.19)
  Would stop it for the moment, while laser position stabilization should cover this
    Further investigation in this week
Emittance break-up at the latter part of the beam transport
    Emittance blow-up several times while the beam goes through BT
  Precise tuning of the beam with new beam monitors like OTR beam profile, etc
  Trying to understand step by step from beam experiments and simulations
Many other items like dispersion corrections, device calibrations, backup device preparation, operation software improvements, etc.

## Slide 7: Examples at the end of linac
After summer
* 7-minute instability
==>
Chiller for a table
* Discrete vertical orbit
==>
New pulsed bend
After Summer
Before Summer
Hor.
Ver.
Charge
Y. Seimiya

## Slide 8: Emittance break-up in BT
Same emittance line
of BT2 as BT1
e- X
e- Y
● Measured by WS
● Emittance due to Jitter
ー Emittance due to BPM res.
ー Emittance due to sd
(invisibly small)
Required emittance
from LER/HER
The horizontal orbit jitter in the e+ is negligibly small.
The other jitter emittances at BT1 is comparable as measured emittance.
But in BT2, all measured emittances are larger than the jitter emittances.
e+X
e+Y
21/Oct
21/Oct
22/Oct
22/Oct
Notes: The emittances due to the measured jitter are plotted by green points.
The green lines show the emittance due to BPM resolution.
They are calculated assumed the design beta.
The pink lines show the emittance due to energy spread by leaked dispersions, which are invisibly small.

## Slide 9
 | 早朝 | 日中 LINAC mode | 準夜 BT dump mode
11/18（水） |  | ２値化問題(パターンを変える。)(夏井) | ~18:00 OTR, BT2 QuadScreen
11/19（木） | QuadBPM(BTp) OctoPos(SY3)e- data taking | 7分変動の調査(吉田) KBP DS Study(三浦) | ~できるまで BT Study
11/20（金） | KBP DC4 response 8:00~9:00e-放射線測定 25Hz Jarc dispersion(吉田) | Jarc dispersion(清宮) 3-5 sector 軌道FB(清宮) | ~できるまで BT Study
11/21（土） | TBD | KBE beam Cleaning | ~18:00 Conditioning KBP DS Study(三浦) 1H MOFB Offの影響を見る
11/22（日） | KBE beam Conditioning | KBE beam Conditioning | KBE beam Conditioning
11/23（月） | KBE beam 1st laser | KBE beam 1st +2nd laser | KBE beam
11/24（火） | KBE beam | HER injection LER injection | 

## Slide 10
Many improvements during summer shutdown and additional items in this week
Injection stabilization is still one of the major challenges for now
Further stabilization expected with existent hardware to help investigation at the beam transport line
Then, pursue several more steps to final designed beams
Thank you

## Slide 11: e- beam V-orbit binarization at LINAC end

## Slide 12: Higher energy injection and collision
Mitigation of accelerator structure failures
  Originally designed for 8 MeV/m, but used at 20 MeV/m
  Degradation that lead to high field emission rate and discharges
  Water leaks
  Not only Y(6S) but even Y(4S) could be suffered
4-year plan to fabricate and install new accelerator structures

## Slide 13: New accelerator structures
First batch acceptance of structures (4)
Now being high-power- conditioned
It exceeded our expectations

## Slide 14: Energy
Recent effort to optimize parameters
  10.753 + 0.023/2 GeV could be possible with backups
    e+ : 4.071 GeV, e- : 7.124 GeV
    with 2 nC/bunch
After structure upgrade in 2023 winter
  6S : 11.020 GeV could be reached with backups
    e+ : 4.165 GeV, e- : 7.289 GeV
    with 2-3 nC/bunch
BT limit
    e+ : 4.290 GeV, e- : 8.465 GeV (both coil heating limit)
MR
  No discussion yet, while included in the design
  Easier with Belle II solenoid scaled
  Otherwise, …

## Slide 15: Linac Beam Parameters for KEKB/SuperKEKB
Linac Beam Property Requirements
Final parameters will be updated
Stage | KEKB (final) |  | Phase-I (achieved) |  | Phase-II (achieved) |  | Phase-III (interim) |  | Phase-III (final) | 
Beam | e+ | e– | e+ | e– | e+ | e– | e+ | e– | e+ | e–
Energy | 3.5 GeV | 8.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV | 4.0 GeV | 7.0 GeV
Stored current | 1.6 A | 1.1 A | 1.0 A | 1.0 A | – | – | 1.8 A | 1.3 A | 3.6 A | 2.6 A
Life time (min.) | 150 | 200 | 100 | 100 | – | – | – | – | 6 | 6
 | primary e- 10 |  | primary e- 8 | 1 | 0.5 | 1 | 2 | 2 | primary e- 10 | 4
Bunch charge (nC) | → 1 | 1 | → 0.4 |  |  |  |  |  | → 4 | 
Norm. Emittance | 1400 | 310 | 1000 | 130 | 200/40 | 150 | 150/30 | 100/40 | 100/15 | 40/20
(gbe) (mrad) |  |  |  |  | (Hor./Ver.) |  | (Hor./Ver.) | (Hor./Ver.) | (Hor./Ver.) | (Hor./Ver.)
Energy spread | 0.13% | 0.13% | 0.50% | 0.50% | 0.16% | 0.10% | 0.16% | 0.10% | 0.16% | 0.07%
Bunch / Pulse | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Repetition rate | 50 Hz |  | 25 Hz |  | 25 Hz |  | 50 Hz |  | 50 Hz | 
Simultaneous top-up injection (PPM) | 3 rings (LER, HER, PF) |  | No top-up |  | Partially |  | 4+1 rings (LER, HER, DR, PF, PF-AR) |  | 4+1 rings (LER, HER, DR, PF, PF-AR) | 

## Slide 16: 24th KEKB accelerator review
    Remotely on July 15th and 20th
General recommendations on injector
  Pursue aggressive linac/injector improvements …
Injector recommendations
  Improvements in
    Positron capturing section, positron yield
    Photocathode for RF gun, electron bunch charge
    BT2 for obstacles, beam instrumentations, beam optics
  Mostly in line with planned improvements during summer

## Slide 17: MEXT roadmap and injector
MEXT Roadmap 2020
    HER 2.6 A x LER 3.6 A (original plan before 2020)
      4 nC/bunch, 2 bunch/pulse, 50 Hz, 50% efficiency could have supported 6 minute lifetime in HER/LER
  ➡ HER 2.0 A x LER 2.8 A
    The same condition supports lifetime down to 240 seconds
    although beam quality has to be maintained