## Slide 1: Electron / Positron Injector Linac
K. Furukawa
for Linac division

## Slide 2: Linac in SuperKEKB Project
40-times higher Luminosity
  Twice larger storage beam  Higher Linac beam current
  20-times higher collision rate with nano-beam scheme
     Low-emittance Linac injection beam
     Shorter storage lifetime  Higher Linac beam current
Linac challenges
  Low emittance e-
    High-charge RF-gun
  Low emittance e+
    Damping ring
  Higher e+ beam current
    New capture section
  Beam transport
  Four ring manipulation
2x beam current
40x Luminosity
RF-gun
e+ increase
Linac Overview
Notes: Higher Injection Beam Current
  To Meet the larger stored beam current and shorter beam lifetime in the ring
  4~8-times larger bunch current for electron and positron
  Reconstruction of positron generator, etc
Lower-emittance Injection Beam
  To meet nano-beam scheme in the ring
  Positron with a damping ring
  Electron with a photo-cathode RF gun
  Emittance preservation by alignment and beam instrumentation
Quasi-simultaneous injections into 4 storage rings
  SuperKEKB e–/e+ rings, and light sources of PF and PF-AR
  Improvements to beam instrumentation, low-level RF, controls, timing, etc

## Slide 3: SuperKEKB Injector Linac
Higher Injection Beam Current
  To Meet the larger stored beam current and shorter beam lifetime in the ring
  4~8-times larger bunch current for electron and positron
  Reconstruction of positron generator, etc
Lower-emittance Injection Beam
  To meet nano-beam scheme in the ring
  Positron with a damping ring
  Electron with a photo-cathode RF gun
  Emittance preservation by alignment and beam instrumentation
Quasi-simultaneous injections into 4 storage rings
  SuperKEKB e–/e+ rings, and light sources of PF and PF-AR
  Improvements to beam instrumentation, low-level RF, controls, timing, etc
Linac Overview

## Slide 4: Linac and Positron Capture Section
4.0 GeV e+ 4nC x 2
3.5 GeV
10nC x 2 (prim. e-)
5nC x 2 (inj. e-)
1.1 GeV
Damping Ring
circ. 136 m
ECS
high current
gun
Energy-spread
Compression System
Bunch
Compressor
7.0 GeV e-
5nC x 2
low emittance
RF gun
SuperKEKB injector Linac
e+ target &
L-band+LAS
capture section
50 Hz (e+ or e-)
pulse-by-pulse
mode switching
S-band
linac
2.5 GeV e-
0.1nC x 1
PF
HER
LER, AR
AR (later)
6.5 GeV e-
C-band
modules
1-4
1-8
2-1
2-8
3-2
1-3
1-5
1-6
1-7
2-2
2-3
2-4
2-6
2-7
target
solenoid
L-band
LAS Large Aperture S-band
FODO singlet system
Q triplet 3m
Q triplet 5m
DR
normal S-band
positron target relocation from 2-1 to 1-5
for energy margin in DR injection
3T
RF gun
Positron Capture Section
Linac Overview and Positron Capture

## Slide 5: Design of Positron Capture Section
KEKB e+ capture section
SuperKEKB e+ capture section
QWT system (2.0 T x45mm + 0.4 T x8m) air-core pulse coil DC solenoids
KLY1 (S-band) -> 2 x 1m 12 MV/m, aper 2a = 27 -> 25 mm
KLY2 (S-band) -> 2 x 2m 10 MV/m, aper 2a = 25 -> 21 mm
beam energy at capture section exit : 80 MeV
AMD system (6.0 T x200mm + 0.4 T x15m) flux concentrator DC solenoids
L-band -> 2 x 2m 10 MV/m, aper 2a = 39 -> 35 mm LA S-band -> 4 x 2m 10 MV/m, aper 2a = 32 -> 30 mm
beam energy at capture section exit : 110 MeV
full L-band configuration
L-band + LAS configuration
for comparable performance
with reduced cost
N(e+)/N(e-) = 65 % at 1.1 GeV DR
N(e+)/N(e-)/E(e-) = 19 %/GeV
N(e+)/N(e-) = 10 % at 3.5 GeV linac-end
N(e+)/N(e-)/E(e-) = 2.5 %/GeV
Deceleration mode
Positron Capture

## Slide 6: Flux Concentrator BINP-type
In collaboration with BINP, prototype field measurement & high-power operation test performed at KEK from Nov. 2010 to March 2011.
Breakdown issue with vacuum burst above 7 Tesla was identified. However, the investigation with BINP experts was interrupted by the Earthquake.
Positron Capture

## Slide 7: Flux Concentrator SLAC-type
with helps from SLAC and IHEP we are going to fabricate SLAC-type FC for linac commissioning from 2013 autumn and stable operation at T=0.
Final optimization of field design and mechanical design as well as fabrication system design
SLAC-type FC at IHEP
Positron Capture

## Slide 8: Capture by L-band and LAS structures
L-band
  Large aperture (d=39~35mm) of accel. structure is desirable for transverse acceptance of Positron Capture Section
  Coprime (5:11) frequency relation is effective to sweep out satellite bunches critical to DR radiation shield issue. Full S-band (LAS) capture section gives comparable e+ yield, but with plenty of satellite particles
LAS (Large Aperture S-band)
  Medium large aperture (d=32~30mm) is desirable for transverse acceptance of PCS and quad focusing system
  Existing S-band rf source, SLED, DC solenoids are available & compact Q at FODO (reduction in initial cost)
Positron Capture

## Slide 9: L-band Klystron
40 MW L-band(1298 MHz) klystron PV-1040 designed by KEK and Mitsubishi Electric
compatible with existing S-band modulator and KLY tank in KEKB linac
first PV-1040 delivered in March 2010
performance test since June 2011
KLY operation spec. at SKB linac 30 MW x 1.5 us x 50 pps achieved !
another two PV-1040 will be delivered, we will have three L-band klystrons for (1) positron capture section (2) bunch compressor at DR (3) spare
(KLY data by S. Matsumoto)
Positron Capture

## Slide 10: L-band Accelerating Structure
first L-band structure completed in March 2010
operation test at test stand from April 2012
RF frequency 1298 (=2856 x5/11) MHz
traveling-wave structure (short rf pulse)
constant gradient
(2/3)pi phase advance per cell
structure length 2.2 meter
disk aperture 2a = 39.4 ~ 35.0 mm
field strength 12 MV/m@15 MW input
single feed coupler (with field symmetrized)
attenuation constant tau = 0.26
(structure data by T. Higo)
Positron Capture

## Slide 11: Built-in Collinear RF Power Load
L-band rf coupler limits DC solenoid inner radius >= 180 mm
for regular cell region, the radius can be 130 mm
with built-in collinear power load, the output coupler can be omitted and end-tail becomes thin
Positron Capture

## Slide 12: Large Aperture S-band Structure
LAS structures are used,
  in second unit of capture section
  in two accelerator modules just behind capture section
Large aperture and compact outer diameter
  existing rf source available
  existing DC solenoid available
  compact quad outside LAS structure compared with L-band
Cost-performance balance
traveling-wave structure
constant gradient
(2/3)pi phase advance per cell
structure length 2.2 meter
disk aperture 2a = 31.9 ~ 30.0 mm
field strength 16.4 MV/m with SLED 6.9 MV/m w/o SLED
two port input coupler (J-shape side-couple) two port output coupler (ordinary shape)
attenuation constant tau = 0.112
Positron Capture

## Slide 13: Solenoid Field Design
FC + DC solenoid field distribution determines transverse acceptance of capture section and e+ initial emittance.
FC + DC Solenoid field
peak ~ 6 Tesla
DC solenoid field
(long range)
Positron Capture

## Slide 14: Particle Simulation
capture section : Zang Lei (GPT), T.Kamitani(EGS4, CST)
linac 1~2 sector + LTR : T.Miura, N.Iida (SAD)
DR beam dynamics : H.Ikeda
RTL + linac 3~5 sector + BT-line : N.Iida (SAD)
Acceleration phase mode
in capture section
Deceleration phase mode
in capture section
Simulation Example
from target to capture section exit (120 MeV)
Energy (MeV)
Energy (MeV)
longitudinal position (mm)
longitudinal position (mm)
Positron Capture

## Slide 15: ECS at LTR & BCS at RTL
Energy-spread
Compression
System
Bunch
Compression
System
ECS reduce energy-spread of e+ entering DR
BCS reduce bunch-length of e+ extracted from DR
R56 = -0.61 m
Vc = 41 MV (S-band)
compression 1/3
Vc = 37 MV (L-band)
R56 = -1.05 m
compression 1/9
non-isochronous arc +
energy correction by RF field
energy gradient by RF field
+ non-isochronous arc
schematic view
scale is not precise !
LTR
RTL
Positron Capture

## Slide 16: Injector Positron Source Status
Fabricating SLAC-type FC for T=0
Need consideration on target protection
1st L-band structure to be high-power tested soon
Design of L-band collinear load fixed
Waveguides & loads in fabrication
L-band klystron 1st tube ready
Large Aperture S-band structures in fabrication
DC solenoid field dips are moderated by huge solenoids
Beam optical design almost OK
Particle tracking simulation is ongoing for e+ yield and hardware parameter optimization
Damping Ring, ECS, BCS are in construction
Positron Capture

## Slide 17: RF Gun at 32 unit for 5nC / 20mm-mrad
Emittance of 300mm in KEKB should be reduced to 20mm
Laser
RF Gun

## Slide 18: Laser Development
Oscillator
  Nd:YAG medium, LD excitation
  Change frequency from 114MHz to 52MHz
    Synchronized through 10.39MHz Clock
  Successful stable excitation
Amplifier improvements
  ~1.5mJ / 30ps / pulse at 266nm
RF Gun

## Slide 19
Nd:YAG
R=0.5m
f=250mm
Output
λ/4
R=0.5m
f=250mm
Input
R=99%
PD
Laser Amplifier Development
RF Gun

## Slide 20: Laser Amplifier Development
Multi-pass
Amplification
Cleaner
Amp.
with
EO and AO
components
RF Gun

## Slide 21: Photo Cathode Development
Started with LaB6
  Successful up to ~0.3nC before April
Replaced with Ir5Ce
  For better quantum efficiency
  Achieved up to ~1nC / bunch in April
Surface cleaning cut & try
  With high power laser with/without RF
  LaB6 and Ir5Ce are rather stable
Other possibilities in the future
  CsTe, etc
RF Gun

## Slide 22: Slant Laser Injection
Perpendicular laser injection
  Before May.2012
Slant laser injection through CaF2 windows
  Non-zero perpendicular electric field (?)
  Increased up to ~3nC / bunch
  Emittance should be confirmed
Chart: polarization angle (degree)
| 0.0 | 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 95.0 | 100.0 | 110.0 | 120.0 | 130.0 | 140.0 | 150.0 | 160.0 | 170.0 | 180.0
 | 0.50141 | 0.54411 | 0.69683 | 0.76093 | 0.8424 | 0.90555 | 0.9288 | 0.95647 | 0.96804 | 1 | 0.97257 | 0.94891 | 0.92905 | 0.84388 | 0.75977 | 0.70256 | 0.62186 | 0.51972 | 0.49742 | 0.4644
Polarization dependence (Ir5Ce)
(東工大/佐藤)
RF Gun

## Slide 23: Stable Operation of RF Gun
DAW (Disk and washer) type photo cathode RF gun
  Strong RF beam focusing
  With stable cathode
  Should experience continuous PF injection in autumn 2012
  With backup laser
Electric field and beam tracing simulation
RF Gun

## Slide 24: Fast Recovery at Failure of Positron Generator
Positron capture section replacement
  How components should be designed/installed in order to be replaced under high radiation condition? (replaced twice in KEKB)
  Positron target, Flux concentrator, Bridge coil, Acceleration structure, Solenoid, Girders, Vacuum components, etc.
  Large unit should be replaced with special links
  Under discussion
Fast Recovery

## Slide 25: Reliability with Failed Acceleration Unit
Linac Beam Energy Management
  At least one backup acceleration unit should available with two units for an energy knob in regions of ;
    Before 180deg arc before damping ring after damping ring
  In each of electron and positron modes (and PF/PF-AR)
  The plan was fixed
  While troubles at several important units (like capture section) can prevent operation, others should be backuped
Reliability with Energy Management

## Slide 26: Beam Position Monitor Development
Requirement
  50Hz with event synch., 2bunchs 96ns apart, 10micron resolution, 0.1~10nC variation at 50Hz
Present system
  8bit oscilloscope, Windows-EPICS, 50Hz,
  50~100micron resolution
BPM is essential for
  Low-emittance transport with wakefield compensation
  Beam stability monitor
BPM

## Slide 27: BPM Development
Modifications to commercial module Libera
  Event-based control capability and embedded EPICS
  Fast attenuator for variable beam modes
  Modifications to filters and ADCs for 2-bunches 96ns apart
New development at local company
  In VME form factor, with external CPU and event-based controls
  Additional on-line pulse test capability
Both evaluations in this year
  Lab tests during summer
  Beam tests in autumn
  Resolution, price, reliability, flexibility, manageability, etc
  Installation in 2014
band-pass + saw filters
BPM

## Slide 28: 4 Ring Injection Timings
SuperKEKB will have integer RF clock relation with Linac
  Needs ring circumference compensation with frequency modulation
PF / PF-AR will not have common clock with Linac
  As they need independent circumference compensation
  Linac injects beams at accidental synchronization
  No synchronization opportunity if integer relation
Damping ring and L-band introduction
  Requires further condition restrictions
Four Ring Injection and PF Sync.

## Slide 29: PF Synchronization
PF Frequency modulation in a year
  Approx. 2 x 10^-5
Four Ring Injection and PF Sync.

## Slide 30: Injection Synchronization with 114MHz
For PF
with KEKB
Duration Jitter
20ms
+/-500μs
Clock Jitter
500 ps
Plot in 10-4
No problems
Four Ring Injection and PF Sync.

## Slide 31: Injection Synchronization with 10.39MHz
For PF with
SuperKEKB
Duration Jitter
20ms
+/-500μs
Clock Jitter
500 ps
Plot in 10-4
Bad region
have to be
avoided
Four Ring Injection and PF Sync.

## Slide 32: Investigation
This issue is different than the bucket selection challenges at SuperKEKB
  Bucket selections both at DR and MR
Was not well investigated under 10.39MHz
  May require pulse-to-pulse LLRF manipulation between RF systems of PF / PF-AR / SuperKEKB
  Should be investigated further
Four Ring Injection and PF Sync.

## Slide 33: Event System Development Collaboration with SINAP
For PLC (F3RP61 Linux CPU) as well as VME
Under testing
Many more synchronous controls at a reduced cost

## Slide 34: Facility for Electric Power and Cooling Water
Linac needs electricity and cooling water extensions, especially for positron generator upgrade
First estimation was performed, and was found that it may impact the construction
Under discussion how to extend the facility
[I] 第1～2セクター
陽電子ビーム強度の５倍化に向けて、収束用電磁石の数と強度が大幅に増加する。
増加分920 kVA, 900 L/min
現状 401kVA
1211 / 1430 L/min
[II] 第3セクター
DRの入射＆出射路の新設に伴って、その電磁石の一部が入射器トンネルに新たに設置される。
増加分310 kVA
現状 6.7kVA
136 / 500 L/min
[III] 第３スイッチヤード
１）陽電子エネルギーの増大（3.5GeV→4GeV）に伴う偏向磁石系の電力増及び ２）RF偏向によるエミッタンスモニターの新設に伴って熱負荷が増大する。
増加分300 kVA, 460 L/min
現状 158kVA
（587+α）/ 750 L/min
Facility

## Slide 35: Schedule
Summer 2012 : Alignment, SY3, 3T-gun, 32-gun
Autumn 2012 : 32-RF-gun, A1-gun(0.2nC)
Winter 2013 : SY2 / DR
Spring 2013 : A1-gun
Summer 2013 : Installation of many components
Autumn 2013 : e– then e+ commissioning
  Half Linac: PF injection, Day: construction, Night: commissioning
Spring 2014 : Pulsed Quad, Steering, Alignment
Summer 2014 : Installation of remainings
Autumn 2014 : Possible ring injection (?)
Winter 2015 : DR then MR injection commissioning
…
Schedule

## Slide 36: Change in Operation Modes at KEKB
May.2000
Apr.2003
Dual Bunch e+
Feb.2005
Continuous
Injections
Dec.2008
Crab Cavities and
Simultaneous Injection
Belle/KEK
Linac provided basis of robust operation
and daily advances in KEKB
So in SuperKEKB as well
KEKB
Summary

## Slide 37
Thank You for Your Patience
Thanks