## Slide 1: 入射器：Phase I運転実績と今後の課題
Masanori Satoh (KEK Acc. Lab. Div. V)
On behalf of Linac Commissioning Group
第110回Bファクトリー計画推進委員会, 2016年7月19日(火)

## Slide 2: 報告内容
概要
SuperKEKB入射器への要求
Phase I コミッショニング
Phase II コミッショニングに向けての課題
まとめ

## Slide 3: 概要
入射器
  4リングへビーム(e-/e+)供給
  600 m長, ビーム繰り返し: 25 Hz (最大: 50 Hz)
  2バンチ運転 (96 ns間隔)
SuperKEKB MR:
  HER: e-, 7 GeV, 1 nC
  LER: e+, 4 GeV, 0.4 nC
放射光リング:
  PF: e-, 2.5 GeV, 0.3 nC
    1日3回入射(場合によりトップアップ)
  PF-AR: e-, 3 GeV, 0.3 nC
    1日3回入射
    (*) 入射後6.5 GeVまで加速
SuperKEKB

## Slide 4: SuperKEKB入射器への要求
低エミッタンスe-/e+ビーム供給:
  e-: 1 nC, 300 mmmrad (KEKB) => 5 nC, 50 (H)/20 (V) mmmrad (Phase III)
  e+: 1 nC, 1500 mmmrad (KEKB) => 4 nC, 100 (H)/20 (V) mmmrad (Phase III)
    (*) Phase I: 1 nC, 低エミッタンス不要, Phase II: 2 nC, 低エミッタンス
  低エミッタンス光陰極RF電子銃 (Ir5Ce, 擬似進行波空洞)
  陽電子ダンピングリング
  精密機器アライメント (0.1 mm – 0.3 mm (s))
  精密軌道測定および制御に基づくエミッタンス保存
大強度e+: フラックスコンセントレータ, 大口径Sバンド加速管
イベントタイミングシステム (バケット選択 MR/DR)
高速RFモニタ，高精度BPM読み出し系，パルスQuad，パルスステアリング
同時トップアップ入射 (短ビーム寿命)
  HER/LER (+ ダンピングリング), PF, およびPF-AR

## Slide 5: 主要パラメタ
 | KEKB (final) |  | SuperKEKB (Phase-I) |  | SuperKEKB (Phase-III) | 
ビーム | e+ | e– | e+ | e– | e+ | e–
エネルギー (GeV) | 3.5 | 8.0 | 4.0 | 7.0 | 4.0 | 7.0
蓄積電荷量 (A) | 1.6 | 1.1 | 1 | 1 | 3.6 | 2.6
寿命 (分) | 150 | 200 | 100 | 100 | 6 | 6
バンチ電荷量 (nC) | Primary e-10 → 1 | 1 | Primary e- 8 → 0.4 | 1 | Primary e-10 → 4 | 5
規格化エミッタンス (mm∙mrad) | 1400 | 310 | 1000 | 130 | 100/20 (Hor./Ver.) | 50/20 (Hor./Ver.)
エネルギー広がり (%) | 0.125 | 0.125 | 0.5 | 0.5 | 0.1 | 0.1
バンチ数 | 2 | 2 | 2 | 2 | 2 | 2
ビーム繰り返し (Hz) | 50 |  | 25 |  | 50 | 
トップアップ | 3 rings (KEKB e–/e+, PF) |  | n/a |  | 4+1 rings (SuperKEKB e–/e+, DR, PF, PF-AR) | 

## Slide 6: 入射運転方式
low emittance
RF gun
A
B
C
1
2
3
4
5
1.5 GeV e-
e+ target
e-:Chicane
4 nC (10 nC) x 2 bunches x 50 Hz (SuperKEKB e+)
5 nC x 2 bunches x 50 Hz (SuperKEKB e-)
0.3 nC x 1 bunch x 25 Hz (PF-AR e-)
0.3 nC x 1 bunch x 25 Hz (PF e-)
1.1 GeV
DR
Decelerate
e+ target
5
4
3
2
1
C
e-
e+
1.1 GeV
4.219 GeV
1.5 GeV
same energy
e-/e+ beams are delivered to 4-rings with different bunch charge and energy.
Beam acceleration modes must be switched by 50 Hz pulse-by-pulse for top-up injection.
HER: 7 GeV e-
PF-AR: 6.5 GeV e-
PF: 2.5 GeV e-
LER: 4 GeV e+
5 nC x2
0.3 nC x1
0.3 nC x1
4 nC x2
パルスQ (ダブレット)
(20 msごとに切り替え)
全ビーム共通設定 (DC Quads)

## Slide 7: 低エミッタンス保存
低エミッタンス電子ビーム輸送（ダンピングリングなし）
精密ビーム軌道操作によるエミッタンス保存
計算機シミュレーションおよびビームによるフィージビリティスタディ
ビームジッタの抑制が重要
- 計算機シミュレーション -
Q, 加速管ミスアライメント: 0.3 mm (s)
50種の異なるミスアライメント
全種補正可能
- ビームスタディ -
熱電子銃
Aセクタにけるステアリング制御
Bセクタ終端においてエミッタンス測定

## Slide 8: 同時トップアップ入射 (3リング)
蓄積ビーム電流値安定性 (2000年) - KEKB: 300 mA (~ 50%)
- PF: 240 mA (~ 53%)
蓄積ビーム電流値安定性 (2010年4月) - KEKB: 1 mA (~ 0.05%) : e-: 12.5 Hz, e+: 25 Hz
- PF: 0.05 mA (~ 0.01%) : 0.5 Hz
KEKB e-
KEKB e+
Luminosity
PF
PF-AR入射中(1日2回,各20分)KEKBトップアップが中断される
短ビーム寿命のSuperKEKBでは大きな問題になる

## Slide 9: PF-ARを含めた同時トップアップ入射
PF-AR/KEKBは，ビーム輸送路を共有
既存のトンネルスペースの問題
PF-AR直接入射路は，2014年5月にトンネル工事完了
振り分けライン（入射器第3スイッチヤード）の工事
2017年2月にコミッショニング予定
H. Takaki (KEKB review 2013)

## Slide 10: 入射器 Phase I コミッショニング
熱電子銃の再インストール（2015年4月)
  陽電子生成用1次電子生成(10 nC)のため
    RF電子銃での最大生成電荷量は 5.6 nC
  RF電子銃ラインはそのまま保持 (1200 mm)
  熱電子銃用ビームラインを新設 (1950 mm)
熱電子銃コミッショニングは2015年5月に完了
SuperKEKB MR (HER/LER) Phase Iコミッショニングは，熱電子銃を用いて開始
6/8(金) ～6/18(土):
  RF電子銃を用いたHER入射 (LER入射は熱電子銃のまま）
  (*) 6/18(土) 13:30: 空調機からの水漏れにより，発信器が停止した。

## Slide 11: 熱電子銃 (HER入射)
運転例:
  1 nC (電子銃), 1 nC (入射器終端), 0.5 nC (BT終端)
  12.5 Hz, 1バンチ
x (mm)
y (mm)
I (nC)
BT
Linac
First bunch
~ 8 ps
(streak camera measurement)

## Slide 12: 熱電子銃 (LER入射)
運転例:
  1次 e-: 10 nC (電子銃), 7 nC (e+標的)
  e+: 0.7 nC (入射器終端), 0.4 nC (BT終端)
  25 Hz, 2バンチ
First bunch
~ 15 ps
(streak camera measurement)
x (mm)
y (mm)
I (nC)
Second bunch
~ 15 ps
(streak camera measurement)
BT
Linac

## Slide 13: 熱電子銃 (MR入射)
1バンチ入射
2バンチ入射
LER:
  入射率: ~ 0.5 mA/s, 入射効率: 70% ~ 100%
HER:
  入射率: ~ 0.8 mA/s, 入射効率: 80% ~ 100%

## Slide 14: 熱電子銃 (エミッタンス測定)
e- beam
e+ beam
マルチワイヤスキャナ (5セクタ)
e-ビーム: enx ~ 160, eny ~ 300 (mm·mrad)
e+ビーム: enx ~ 1000, eny ~ 1200 (mm·mrad)

## Slide 15: コミッショニングツール
全パラメタはEPICS PV経由にて制御可能
  ~ 150 IOCs
パラメタロギング: Channel Archiver, CSS Archiver
  42000 PVs
  CLIおよびWebベースデータブラウザ
EPICS CSSアラームによる異常データ監視
SAD, Python, CSSベースのツール群
パラメタ管理ツール
モデルおよび測定レスポンスを基にした軌道補正/FB
エネルギーFB用 EPICS IOC
エネルギー広がりモニタおよびFB
同期BPM測定ツール (Shot ID)
高速RFモニタによる同期測定ツールの開発および同期BPM測定との連携
オンライン解析ツール

## Slide 16
バンチ圧縮あり
バンチ圧縮なし
Injection tuning
RF電子銃によるMR入射
HER current (mA)
Injection efficiency (%)
Bunch charge (nC)
A1ユニット試験でのバンチ圧縮後，入射効率はほぼ100%を達成した。

## Slide 17
RF電子銃による安定なHER入射
24時間
HER電流値
LER電流値
入射率
入射効率

## Slide 18
RF電子銃によるビーム軌道
(バンチ圧縮なし)
Horizontal steering x (A)
Vertical steering x (A)
BT
Linac
x (mm)
y (mm)
I (nC)

## Slide 19
RF電子銃によるビーム軌道
(バンチ圧縮あり)
x (mm)
y (mm)
I (nC)
Horizontal steering x (A)
Vertical steering x (A)
BT
Linac

## Slide 20: エミッタンス (RF電子銃)
RF電子銃を用いたMR入射 (2016年5月31日(金))
バンチ電荷量 1 nC (エミッタンス保存無し）
Qスキャン(Qscan)およびマルチワイヤスキャナ(WS)によるエミッタンス測定
Qスキャン測定は，プロファイルモニタおよびトリガ同期機能付きGbEネットワークカメラを使用
測定場所 | 水平方向 en,x (mm·mrad) | 垂直方向 en,y (mm·mrad)
A1ユニットシケイン (Qscan) | 28.3 | 26.4
A1_M (Qscan) | 20.3 | 17.7
Bセクタダンプ (Qscan) | 48.5 | 21.7
Cセクタ (WS) | 100 ± 138 | 34.2 ± 16.5
5セクタ (WS) | 106 ± 24.9 | 76.5 ± 38.9
BT (WS) | 211 ± 110.6 | 133 ± 22.2

## Slide 21
RF電子銃を用いたHER入射: 7/8(金)～
バンチ電荷量の変動は4% ~ 5%. (~ 20% in 2014)
  1% ~ 2% (熱電子銃)
バンチ電荷量の変動は，ビーム繰り返しに依存しない
バンチ電荷量安定性 (RF電子銃)

## Slide 22
位置安定性は，ほぼ熱電子銃ビームと同等
水平方向は垂直方向より変動が大きい
sx,y: 0.1 mm ~ 0.2 mm (熱電子銃)
ビーム位置安定性 (RF電子銃)

## Slide 23: Phase II コミッショニングに向けての課題
低エミッタンスビームの確立 (2 nC, 20 mm·mrad)
  RF電子銃 (2 nC, 10 mm·mrad)
  プレアライメントおよび床変動への対抗策
  低エミッタンス保存
    高精度BPM読み出し系への更新 (91台中36台更新). s ~ 50 mm => 5 mm)
    低エミッタンス軌道探索
    ビームジッタ源の特定および除去
  コミッショニングツールの整備
大強度陽電子生成
  12 kA運転に向けた新フラックスコンセントレータ (ワークハードニング処理）の設置 (2016年秋）
同時トップアップ運転 (HER, LER (+ damping ring), PF, PF-AR)
  新PF-ARビーム輸送路のコミッショニング (2017年2月)
  パルスQ (30台), パルスステアリング (36台)の設置 (2017年夏)
  安全系システムの改修 (同時トップアップ運転に向けて）

## Slide 24: 軌道不安定性 (RF電子銃)
x (mm)
y (mm)
I (nC)

## Slide 25: 軌道不安定性 (熱電子銃)
x (mm)
y (mm)
I (nC)

## Slide 26: パルスQ ビーム試験

## Slide 27: まとめ
Phase I コミッショニングに向けた熱電子銃の再設置をおこなった 。(2015年5月)
SuperKEKB MR Phase I コミッショニングは，HER/LER入射ともに熱電子銃を用いて開始し，大きな問題も無く終了した。
RF電子銃を用いたMR入射に初めて成功し (2016年5月31日(火))，連続的に入射をおこなった。
Phase II コミッショニングに向けて，残された課題を一つずつ解決していく。

## Slide 28: Backup

## Slide 29: Emittance growth due to component misalignment
Sector Cto5: -10 deg rf phase R56 =-0.20
Simulation results from 100 different seeds.
Misalignment of Quadrupole magnets and Accelerating structure:
  s < 0.1 mm: bge 20 mm·mrad is almost satisfied.
  s > 0.1 mm: emittance preservation is required by some methods.
20 mm·mrad
<Emittance growth>
・quadratic curve as a function of misalignment
・final emittance depends on error seed
Norm. projected rms emittance (mmmrad)
Misalignment s (mm)
Simulation
SAD code, Elegant
Initial bunch charge: 5 nC
Initial emittance: 6 mmmrad
Initial bunch length: 10 ps (FWHM)
Initial energy spread : 0.4%
Initial beam energy: 20 MeV
Uniform longitudinal beam distribution

## Slide 30: Energy spread requirement
For the synchrotron phase space injection, small energy spread (0.1%) is required.
A rectangular beam distribution in the longitudinal direction is required for the beam with bunch charge of 5 nC (Phase III).
Laser shaping technique (temporal manipulation)
S. Kazama et al., IPAC’15, MOPWA053
Rectangular shape
Gaussian shape
0.1

## Slide 31: Offset injection (experiment)
Feasibility of offset injection was studied w/ bunch charge of 0.3 nC (thermionic gun).
Changing the excitation current of steering magnet at Unit A4.
Emittance was measured multiple wire scanner at Sector B end.
We will conduct this measurement w/ rf gun.

## Slide 32: Emittance w/ bunch charge fluctuation
Emittance simulation w/ 10 misalignment seeds (accelerating structure).
Sector C to Sector 5 (Linac end)
Assuming 5 nC, initial emittance of 10 mmmrad (SectorC)
When bunch charge increases by 10%, emittance increases by 6.5%.
Try simulations w/ measured component misalignment, dynamic beam line movement, energy jitter.
5 nC => 5.5 nC
12.4 => 13.2 mmmrad

## Slide 33: Emittance measurement
Emittance as function of bunch charge (drop the results w/ large error )
Small bunch charge (< 1 nC) shows good emittance at injector section.
  < 10 mmmrad (Vertical), < 15 mmmrad (Horizontal)
Results at SectorB show larger emittance than our goal.
20

## Slide 34: Optics design
Quadrupole triplets will be installed in merger line.
Beam size is not so large in comparison with bore radius of vacuum chamber .
(mm)
Ver. beam size (mm)
Hor. beam size (mm)
Beam energy (MeV)
Merger line

## Slide 35: Beam diagnostics
Beam position measurement
  BPMs x 91 (strip-line type electrodes)
Beam profile/Emittance measurement
  Fluorescent screen monitors x100
  Single wire scanner x1
  Multiple wire scanner x5
Bunch length measurement
  Streak camera x3

## Slide 36
New BPM readout system
Current system:
  Windows-based digital oscilloscope
    10 GSa/s, 8 bit, 1 GHz bandwidth, 4 channels
    Twenty four systems process the signals from 92 BPMs
    Position measurement precision: 25～50 mm (3-BPM method)
New system:
  VME module w/ band-pass sampling scheme
    250 MSa/s, 16 bit ADC,
    BPF (fc: 180 MHz, BW: 60 MHz, 22 MHz)
    Signal can be well damped within 80 ns
    (first and second bunch interval: 96 ns)
  Measurement precision: 3 mm
  104 modules have been manufactured.
  12 modules have been successfully utilized for daily operation.
80 ns

## Slide 37: Profile monitor
Screen material is made of 99.5% Al2O3 and 0.5% CrO3 (AF995R, Demarquest Co.). (t: 1 mm)
Linux/PLC (x31) control profile monitor (insert/remove, video signal select, limit switch, LED illumination, pneumatic air pressure).
EPICS IOC is running on Linux/PLC. HLA is implemented by Python.
Controller and HLA
Beam profile
Monitor and CCD camera

## Slide 38: Profile monitor (cont’d)
7/97 were replaced by 30-mm-thick one for precise beam size/emittance measurement (Quadrupole scan).
CCD cameras have been replaced by new one.
  Allied Vision: GC650 w/ GbE
  Ext. trigger input
  EPICS IOC, CSS for HLA

## Slide 39: Bunch charge history (rf gun)
0.75 nC
5.6 nC

## Slide 40: Bunch compression at Unit-A1
A1 RF F 0°: 30 ps
w/o bunch compression
30 ps
Chicane
Laser length
30 ps
A1 RF F -30°: 10 ps
w/ bunch compression
10 ps

## Slide 41: Bunch charge from rf gun in last Dec.
1 week

## Slide 42: Typical beam charge stability
1 hour
sI: 10% ~ 20%
~ 2.5% (KEKB operation)

## Slide 43: Bunch charge and laser power
Laser power (Arb. Units)
Bunch charge (nC)
Bunch charge (1st BPM) as a function of laser power.
Clear correlation between them

## Slide 44: Bunch charge fluctuation
Bunch charge fluctuation as a function of bunch charge (2D histogram)
Oct. of 2013 – Dec. of 2014
Requirement for Phase-I

## Slide 45: e- beam parameters
 | SuperKEKB | KEKB
Energy (GeV) | 7.0 | 8.0
HER stored current (A) | 2.6 | 1.1
HER beam lifetime (min.) | 6 | 200
Maximum beam repetition (Hz) | 50 | 50
Max. # of bunch in an rf pulse | 2 | 2
Emittance (mmmrad) | 50/20 (Hor./Ver.) | 310
Charge (nC) | 5 | 1
Energy spread (%) | 0.1 | 0.05
Bunch length sz (mm) | 1.3 | 1.3
Damping ring | - | -
Simultaneous top-up injection | 4 rings (SuperKEKB e-/e+, PF, PF-AR) | 3 rings (KEKB e-/e+, PF)

## Slide 46: e+ beam parameters
 | SuperKEKB | KEKB
Energy (GeV) | 4 | 3.5
LER stored current (A) | 3.6 | 1.6
LER beam lifetime (min.) | 6 | 133
Maximum beam repetition (Hz) | 50 | 50
Max. # of bunch in an rf pulse | 2 | 2
Emittance (mmmrad) | 100/20 (Hor./Ver.) | 1400
Charge (nC) | 4 | 1
Energy spread (%) | 0.07 | 0.125
Bunch length sz (mm) | 0.7 | 2.6
Damping ring | 〇 | -
Simultaneous top-up injection | 4 rings (SuperKEKB e-/e+, PF, PF-AR) | 3 rings (KEKB e-/e+, PF)

## Slide 47: Shot-by-shot beam profile stability

## Slide 48: Beam position stability @ SP_A1_C5
Measured beam position at first BPM (SP_A1_C5)
  sx ~ 0.57 mm
  sy ~ 0.11 mm
Fluctuation of horizontal beam position is larger than vertical one.
30 min.

## Slide 49: Energy spread measurement @ J-ARC
Measure beam energy spread by screen monitor (middle of J-ARC) w/ and w/o bunch compression at A1 chicane.
Bunch compression at A1 unit is effective for energy spread compensation.
A1 chicane On
(w/o bunch compression)
A1 chicane Off
(w/ bunch compression)

## Slide 50: Bunch compression @ J-ARC
Isochronous (w/o bunch compression), R56 = -0.3 m (w/ bunch compression) w/ different RF F in SectorA/B
Clear bunch compression has not yet been measured.
Emittance measurement by multiple wire scanner at Sector2 w/ and w/o J-ARC bunch compression.
Streak camera at SectorC

## Slide 51: Bunch compression at J-ARC
Mitigate transverse wakefield and emittance growth
Initial bunch length 10 ps => 5 ps (bunch compression at J-ARC)
  First stage compression at A1 unit (30 ps => 10 ps)
Control R56 and energy spread at J-ARC
Jarc
Bunch compression

## Slide 52: Emittance (misalignment s = 0.3 mm)
Bunch compression is effective.
However, still not enough for 20 mmmrad.
20 mmmrad
R56 = -0.30 (w/ compression)
R56 = 0 (w/o compression)

## Slide 53: Bunch compression at A1 unit
To mitigate space charge effect, bunch length is compressed from
30 ps to 10 ps.
Chicane
Laser hut
First Accelerating structure
Streak
camera
RF gun